## Slide 9
System Timing Diagrams
T-State:
One clock period is referred to as a T-State
T-State
An operation takes an integer number of T-States
CPU Bus Cycle:
A bus cycle consists of 4 or more T-States
T1
T2
T3
T4

## Slide 10
Wait and Idle States
• Idle State
  – No bus activity required
  – Each is 1 clock period long
  – Occurs when instruction queue is full or the MPU does not need to read/write to memory
• Wait State
  – Triggered by events external to MPU
  – Buffer full will trigger a wait state
  – Triggered by READY pin
  – Inserted between T3 and T4

## Slide 16: Memory Segmentation
.
Physical Address
Base Address
Offset
Effective Address
Use of segment registers, and pointers

## Slide 17: Stack Addressing
The 8086 let you set aside an entire 64Kb segment as a stack.
The upper 16 bits of the starting address for this segment are kept in the stack segment register.
The stack pointer register holds the offset (16 bit).
The memory location where a word was most recently stored is called the top of stack.

## Slide 18: Stack Addressing
The physical address for a stack read or a stack write is produced by adding the contents of the stack pointer register to the stack segment register.
Example:
SS = 5000H * 10H = 50000H
SP = FFE0H
SS + SP = 50000H + FFE0H
= 5FFE0H

## Slide 19: Minimum and Maximum Modes
The minimum mode is selected by applying logic 1 to the MN / MX# input pin. This is a single microprocessor configuration.
The maximum mode is selected by applying logic 0 to the MN / MX# input pin. This is a multi micro processors configuration.

## Slide 20: Difference : Min and Max mode

## Slide 21: Minimum Mode Interface
When the Minimum mode operation is selected, the 8086 provides all control signals needed to implement the memory and I/O interface.
The minimum mode signal can be divided into the following basic groups : address/data bus, status, control, interrupt and DMA.
Address/Data Bus : these lines serve two functions. As an address bus is 20 bits long and consists of signal lines A0 through A19. A19 represents the MSB and A0 LSB. A 20bit address gives the 8086 a 1Mbyte memory address space. More over it has an independent I/O address space which is 64K bytes in length.

## Slide 22
8086 Minimum-Mode Signals
Mode
Select MN/MX’
Interrupt
interface
8086 MPU
Power supply
Vcc GND
INTR
_____
INTA
_____
TEST
NMI
RESET
HOLD
HLDA
Address / data bus
AD0-AD15,
A16/S3-A19/S6
ALE
____
BHE/S7
M/IO’
DT/R’
___
RD
___
WR
____
DEN
READY
CLK
DMA
interface
Memory/IO
controls

## Slide 23
System Clock Generator-8284

## Slide 24
8086 Minimum-Mode

## Slide 25
DEN
WR
ADD / DATA
A
15
–
A
0
Valid data D
15
–
D
0
S
7
–
S
3
A
19
–
A
16
BHE
ADD / STATUS
T
1
T
2
T
3
T
W
T
4
T
1
DT / R
Read/Write Cycle Timing Diagram for Minimum Mode
ALE

## Slide 27
CLK
M/IO
ALE
ADDR/ DATA
ADDR/ STATUS
RD/INTA
READY
DT/R
DEN
T1
T2
T3
TW
T4
A15-A0
A19-A16
RESERVED FOR DATA
VALID D15-D0
MEMORY ACCESS TIME

## Slide 28
CLK
M/IO
ALE
ADDR/ DATA
ADDR/ STATUS
READY
DT/R
DEN
T1
T2
T3
TW
T4
A15-A0
A19-A16
DATA OUT (D15-D0)
WR

## Slide 29: Pins and Signals
8086 Microprocessor
Min/ Max Pins
The 8086 microprocessor can work in two modes of operations : Minimum mode and Maximum mode.
In the minimum mode of operation the microprocessor do not associate with any co-processors and can not be used for multiprocessor systems.
In the maximum mode the 8086 can work in multi-processor or co-processor configuration.
Minimum or maximum mode operations are decided by the pin MN/ MX(Active low).
When this pin is high 8086 operates in minimum mode otherwise it operates in Maximum mode.

## Slide 30: Pins and Signals
8086 Microprocessor
 | (Data Transmit/ Receive) Output signal from the processor to control the direction of data flow through the data transceivers
 | (Data Enable) Output signal from the processor used as out put enable for the transceivers
ALE | (Address Latch Enable) Used to demultiplex the address and data lines using external latches
 | Used to differentiate memory access and I/O access. For memory reference instructions, it is high. For IN and OUT instructions, it is low.
 | Write control signal; asserted low Whenever processor writes data to memory or I/O port
 | (Interrupt Acknowledge) When the interrupt request is accepted by the processor, the output is low on this line.
Minimum mode signals

## Slide 31: Pins and Signals
8086 Microprocessor
HOLD | Input signal to the processor form the bus masters as a request to grant the control of the bus. Usually used by the DMA controller to get the control of the bus.
HLDA | (Hold Acknowledge) Acknowledge signal by the processor to the bus master requesting the control of the bus through HOLD. The acknowledge is asserted high, when the processor accepts HOLD.
Minimum mode signals

## Slide 32: Pins and Signals
8086 Microprocessor
 | Status signals; used by the 8086 bus controller to generate bus timing and control signals. These are decoded as shown.
Maximum mode signals

## Slide 33: Pins and Signals
8086 Microprocessor
 | (Queue Status) The processor provides the status of queue in these lines. The queue status can be used by external device to track the internal status of the queue in 8086. The output on QS0 and QS1 can be interpreted as shown in the table.
Maximum mode signals

## Slide 34: Pins and Signals
8086 Microprocessor
Maximum mode signals

## Slide 35
When the 8086 is set for the maximum-mode configuration, it provides signals for implementing a multiprocessor / coprocessor system environment.
By multiprocessor environment we mean that one microprocessor exists in the system and that each processor is executing its own program.
Usually in this type of system environment, there are some system resources that are common to all processors.
They are called as global resources. There are also other resources that are assigned to specific processors. These are known as local or private resources.
Maximum Mode Interface

## Slide 36
Bus Controller - 8288

## Slide 38: 8086 Maximum Mode System

## Slide 40
T
1
T
2
T
3
T
4
T
1
One bus cycle
Active
Active
Inactive
S
7
–
S
3
BHE, A
19
A
–
16
A
15
–
A
0
D
15
–
D
0
ALE
Add/Data
MRDC
DT / R
DEN
Clk
S2 – S0
Add/Status
Memory Read Timing in Maximum mode.

## Slide 41
T
1
T
2
T
3
T
4
T
1
Clk
One bus cycle
ALE
S
2
–
S
0
Active
Active
Inactive
BHE
ADD/STATUS
S
7
–
S
3
A
15
-
A
0
Data out D
15
D
–
0
ADD/DATA
DEN
DT / R
MWTC or IOWC
AMWC or
A
IOW
C
high
Memory Write Timing in Maximum mode.

## Slide 42: Assembler directives

## Slide 43: Assemble Directives
8086 Microprocessor
Instructions to the Assembler regarding the program being executed.
Control the generation of machine codes and organization of the program; but no machine codes are generated for assembler directives.
Also called ‘pseudo instructions’
Used to :
› specify the start and end of a program
› attach value to variables
› allocate storage locations to input/ output data
› define start and end of segments, procedures, macros etc..

## Slide 44: Assemble Directives
8086 Microprocessor
Define Byte
Define a byte type (8-bit) variable
Reserves specific amount of memory locations to each variable
Range : 00H – FFH for unsigned value; 00H – 7FH for positive value and 80H – FFH for negative value
General form : variable DB value/ values
Example:
LIST DB 7FH, 42H, 35H
Three consecutive memory locations are reserved for the variable LIST and each data specified in the instruction are stored as initial value in the reserved memory location
DB
DW
SEGMENT
ENDS
ASSUME
ORG
END
EVEN
EQU
PROC
FAR
NEAR
ENDP
SHORT
MACRO
ENDM

## Slide 45: Assemble Directives
8086 Microprocessor
Define Word
Define a word type (16-bit) variable
Reserves two consecutive memory locations to each variable
Range : 0000H – FFFFH for unsigned value; 0000H – 7FFFH for positive value and 8000H – FFFFH for negative value
General form : variable DW value/ values
Example:
ALIST DW 6512H, 0F251H, 0CDE2H
Six consecutive memory locations are reserved for the variable ALIST and each 16-bit data specified in the instruction is stored in two consecutive memory location.
DB
DW
SEGMENT
ENDS
ASSUME
ORG
END
EVEN
EQU
PROC
FAR
NEAR
ENDP
SHORT
MACRO
ENDM

## Slide 46: Assemble Directives
8086 Microprocessor
SEGMENT : Used to indicate the beginning of a code/ data/ stack segment
ENDS : Used to indicate the end of a code/ data/ stack segment
General form:
Segnam SEGMENT … … … … … … Segnam ENDS | Program code or Data Defining Statements
User defined name of the segment
DB
DW
SEGMENT
ENDS
ASSUME
ORG
END
EVEN
EQU
PROC
FAR
NEAR
ENDP
SHORT
MACRO
ENDM

## Slide 47: Assemble Directives
8086 Microprocessor
DB
DW
SEGMENT
ENDS
ASSUME
ORG
END
EVEN
EQU
PROC
FAR
NEAR
ENDP
SHORT
MACRO
ENDM
Informs the assembler the name of the program/ data segment that should be used for a specific segment.
General form:
Segment Register
ASSUME segreg : segnam, .. , segreg : segnam
User defined name of the segment
ASSUME CS: ACODE, DS:ADATA | Tells the compiler that the instructions of the program are stored in the segment ACODE and data are stored in the segment ADATA
Example:

## Slide 48: Assemble Directives
8086 Microprocessor
DB
DW
SEGMENT
ENDS
ASSUME
ORG
END
EVEN
EQU
PROC
FAR
NEAR
ENDP
SHORT
MACRO
ENDM
ORG (Origin) is used to assign the starting address (Effective address) for a program/ data segment
END is used to terminate a program; statements after END will be ignored
EVEN : Informs the assembler to store program/ data segment starting from an even address
EQU (Equate) is used to attach a value to a variable
ORG 1000H | Informs the assembler that the statements following ORG 1000H should be stored in memory starting with effective address 1000H
LOOP EQU 10FEH | Value of variable LOOP is 10FEH
_SDATA SEGMENT ORG 1200H A DB 4CH EVEN B DW 1052H _SDATA ENDS | In this data segment, effective address of memory location assigned to A will be 1200H and that of B will be 1202H and 1203H.
Examples:

## Slide 49: Assemble Directives
8086 Microprocessor
DB
DW
SEGMENT
ENDS
ASSUME
ORG
END
EVEN
EQU
PROC
ENDP
FAR
NEAR
SHORT
MACRO
ENDM
PROC Indicates the beginning of a procedure
ENDP End of procedure
FAR Intersegment call
NEAR Intrasegment call
General form
procname PROC[NEAR/ FAR] … … … RET procname ENDP | Program statements of the procedure Last statement of the procedure
User defined name of the procedure

## Slide 50: Assemble Directives
8086 Microprocessor
DB
DW
SEGMENT
ENDS
ASSUME
ORG
END
EVEN
EQU
PROC
ENDP
FAR
NEAR
SHORT
MACRO
ENDM
ADD64 PROC NEAR … … … RET ADD64 ENDP | The subroutine/ procedure named ADD64 is declared as NEAR and so the assembler will code the CALL and RET instructions involved in this procedure as near call and return
CONVERT PROC FAR … … … RET CONVERT ENDP | The subroutine/ procedure named CONVERT is declared as FAR and so the assembler will code the CALL and RET instructions involved in this procedure as far call and return
Examples:

## Slide 51: Assemble Directives
8086 Microprocessor
DB
DW
SEGMENT
ENDS
ASSUME
ORG
END
EVEN
EQU
PROC
ENDP
FAR
NEAR
SHORT
MACRO
ENDM
Reserves one memory location for 8-bit signed displacement in jump instructions
JMP SHORT AHEAD | The directive will reserve one memory location for 8-bit displacement named AHEAD
Example:

## Slide 52: Assemble Directives
8086 Microprocessor
DB
DW
SEGMENT
ENDS
ASSUME
ORG
END
EVEN
EQU
PROC
ENDP
FAR
NEAR
SHORT
MACRO
ENDM
MACRO Indicate the beginning of a macro
ENDM End of a macro
General form:
macroname MACRO[Arg1, Arg2 ...] … … … macroname ENDM | Program statements in the macro
User defined name of the macro

## Slide 53: To write an assembly language program to perform division of 16-bit unsigned number by 8-bit unsigned number.
.MODEL SMALL
DATA SEGMENT
OPR1 DW 2C58H
OPR2 DB 56H
RESQ DB ?
RESR DB ?
DATA ENDS
ASSUME CS : CODE, DS : DATA
CODE SEGMENT
START:MOV AX, DATA
MOV DS, AX
MOV AX, OPR1
DIV OPR2
MOV RESQ, AL
MOV RESR, AH
MOV AH, 4CH
INT 21H
CODE ENDS
END START